## Slide 1: The Concept of Seaworthiness in the Context of Arctic Shipping: Reasonably Fit in All Respects?
Seamus Ryder

## Slide 2: Agenda
Concept of Seaworthiness and its application in Marine Contracts
Hazards of the Arctic
Unique Requirements for shipping operations in the Arctic
Discussion on seaworthiness and risk distribution of Arctic voyages

## Slide 3: Seaworthiness
Generally described as “a ship that is reasonably fit to confront the perils of the sea”1
Seaworthiness is a relative or “dynamic” term and is defined with reference to the vessel’s cargo, its intended voyage, hazards likely to be encountered and the vessel’s ability to withstand those hazards 2
The features of a seaworthy vessel change over time as more advanced navigational equipment and technology become available. 3
The notion of seaworthiness now underlines almost all aspects of private maritime law

## Slide 4: Carriage of Goods Contracts
Hague -Visby Rules, Article III:
“The carrier shall be bound, before and at the beginning of the voyage, to exercise due diligence to:
(a) make the ship seaworthy;
(b) properly man, equip and supply the ship;
(c) make the holds, refrigerating and cool chambers, and all other parts of the ship in which goods are carried, fit and safe for their reception, carriage and preservation.”4

## Slide 5: Marine Insurance Contracts
“37 (1)There is an implied warranty in every voyage policy that, at the commencement of the voyage, the ship will be seaworthy for the purpose of the particular marine adventure insured.
(2) Where a voyage policy attaches while the ship is in port, there is an implied warranty in the policy that the ship will, at the commencement of the risk, be reasonably fit to encounter the ordinary perils of the port.
(3) Where a voyage policy relates to a voyage performed in different stages during which the ship requires different or further preparation or equipment, there is an implied warranty in the policy that, at the commencement of each stage, the ship is seaworthy for the purposes of that stage.
(4) There is no implied warranty in any time policy that the ship will be seaworthy at any stage of the marine adventure, but where, with the privity of the insured, the ship is sent to sea in an unseaworthy state, the insurer is not liable for any loss attributable to unseaworthiness.
(5) A ship is deemed to be seaworthy if it is reasonably fit in all respects to encounter the ordinary perils of the seas of the marine adventure insured.”5

## Slide 6: Unique Hazards of the Arctic
The hazards to which Arctic shipping is exposed presents significantly higher risks than in most other trading regions, such as6:
Poor weather conditions and the relative lack of good charts ,communication systems and other navigational aids pose challenges for mariners.
The remoteness of the area makes rescue or clean up operations difficult and costly.
Extreme cold temperatures may reduce the effectiveness of numerous components of the ship, including deck machinery and emergency equipment.
When ice is present, it can impose additional loads on the hull, propulsion system and appendages.

## Slide 7: Shipping Safety Control Zones
Arctic waters are divided into 16 shipping safety control zones. Navigation in each zone is permissible only for designated classes of ships depending on their technical capabilities. 7

## Slide 8: Unique Requirements
Ships intending to operate within Canadian Arctic waters are subject to certain unique requirements in addition to those common to vessels operating elsewhere in Canada, such as 8:
The Arctic Waters Pollution Prevention Act (AWPPA)
The Arctic Shipping Safety and Pollution Prevention Regulations, which contain a range of safety and pollution prevention requirements and also incorporates:
  the International Code for Ships Operating in Polar Waters (Polar Code), with the addition of Canadian modifications to ensure that strict safety measures and discharge requirements are maintained.
  SOLAS Chapter XIV “Safety Measures for Ships Operating in Polar Waters”

## Slide 9: The Polar Code
Goal of the polar code is “to provide for safe ship operation and the protection of the polar environment by addressing risks present in polar waters and not adequately mitigated by other instruments of the organization”. 9
The polar code addresses a wide range of requirements concerning maritime safety, including 10:
  Design: ice strengthened hull, materials suitable for polar temperatures, varying structural requirements based on thickness of ice, stability considering ice accretion
  Equipment: special equipment for ice removal, fire safety & lifesaving equipment operable in cold temperatures, thermal protection
  Operations: navigational aids for ice conditions
  Crew: advanced training for ice infested waters
  Environmental protection: prohibits or strictly limits discharges of oil, chemicals, sewage, garbage, food wastes and many other substances.11
Affected vessels are required to be surveyed and certified according to the polar code and to be issued the Polar Code Certificate 12

## Slide 10: Seaworthiness and the Polar Code
For a vessel entering Arctic waters, can it be concluded that non-compliance with the Polar Code constitutes unseaworthiness for the purposes of the implied warranty in a marine insurance contract?
The answer should be in the affirmative if non-compliance with the Polar Code leads to the vessel not being fit in all respects for its intended purpose, namely, traversing the waters of the Arctic. 13

## Slide 11: Concept of Seaworthiness and the Arctic
Reasonably fit in all respects ?

## Slide 12: Risk Distribution
How will risk be assumed or distributed in a maritime contract involving an Arctic voyage?

## Slide 13: THANK YOU

## Slide 14: References
1 Canadian Maritime Law, Aldo Chircop, 2nd ed, pg. 72
2 Ibid
3 supra note 3, pg. 507
4 Marine Liability Act, Schedule 3, Art III
5 supra note 1, s. 37(1)-(5)
6 International Code for Ships Operating in Polar Waters (Polar Code) (imo.org)
7 Supra note 3, pg. 1010-1011
8 https://www.rcaanc-cirnac.gc.ca/eng/1648145733596/1648145784817
9 Polar Code Ship Safety - Infographic_smaller_.pdf (imo.org)
10 ibid
11 Milestone for polar protection as comprehensive new ship regulations come into force (imo.org)
12 supra note 3, pg. 997
13 “Legal Regime of Marine Insurance in Arctic Shipping: Safety and Environmental Implications”, Proshanto K. Mukherjee and Huiru Liu, pg. 209
Photo on 1st slide: Arctic Shipping Routes Are Feeling the Heat – Eos
Photo on 5th slide: Ice Navigation in Canadian Waters (dfo-mpo.gc.ca)
Photo on 11th slide: https://pame.is/arctic-shipping